 vxE systematics:
net UCN motion in imperfect E field

---
vxE effect
Starting equation:
(d_{n})_meas = {%epsilon_{ {}+{} }-%epsilon_{ {}-{} }}over { 4E }
sin(α)BvxE
%epsilon_{ {}+-{} }=2 %mu_n B_{{}+-{}} +-2 d_n E_{{}+-{}}
α
B0
E
Taylor expension: α<<1 BvxE/B0<<1
%epsilon_{ {}+-{} }=2 %mu_n( B_0 +-{ v }over {c²} %alpha E + B_{vxE}^2 over {2B_0})+-2 d_n E
v
(d_{n})_{vxE} =%mu_n over c^2 %alpha v

---
Numerical application
(d_{n})_{vxE} =1.3 10^-24 %alpha v_net
[ecm]
[???]
(d_{n})_{vxE} =%mu_n over c^2 %alpha v
BUT
(d_{n})_{vxE} =6.7 10^-25 %alpha v_net
[ecm]
[e.s-1]
Re analysis paper
Real value

---
Net rotational motion
(d_{n})_{vxE} =6.7 10^-25 {e.cm } over {cm s^-1} %alpha v_net
Re analysis paper
neutron velocity : v0 =1m/s
Coherent motion ~5 s of the cycle
        ~0.1% neutrons
Cycle ~130 s
<v>coh~3.8 cm/s
<v>net~3.8E-3 cm/s
α=0.1 rad
(d_{n})_{vxE} =2.6 10^-28 e.cm

---
Electric field
Marcin Kúzniak Thesis
The net volicity :
(v)net=5mm/s
(MC simulation)
α

---
Conclusion
- Same calculation for most references
- Different (v)net and α …
  How to determine them ?
	α [rad]	Vnet [cm/s]	(dn)vxE [10-28 ecm]
Re analysis paper	<0.1	3.8E-3	<2.6
M. Kúzniak	-0.28 E-3	0.5	-0.94
Zenner	0.005**	0.5	16.9
Guillaume talk	<0.035	<5.6E-3	<1.3
** typo in the thesis corrected

---
Questions?

---
HV simulation nEDM
kV/cm
3D geometry:
UCN hole
Hg hole
Coronna
2 windows
View through the window

---
HV simulation nEDM
kV/cm
View through the mercury hole